TECHNICAL DATA SHEET

PRODUCT NAME: POLTEM PV-800

PRODUCT TYPE: HIGH PERFORMANCE WAX

PRODUCT DESCRIPTION

Poltem PV-800 is a glossy cream wax and using to release the polyester and GRP products from the moulds.

PRODUCT PROPERTIES

| Wax Base | Carnauba, boeswaxes, mineral waxes |
| --- | --- |
| Solvent Base | Aliphatic hydrocarbons |
| Appearance | Glossy, cream paste |

APPLICATION

On the used moulds, apply onto the all mould surface by circular motions and wait for 5-10 minutes to obtain a thin film. After that polish with a piece of clean dry cotton fabric. Keep stand it for 15-20 minutes in order to get dry. Finally wipe and polish with a clean cotton fabric.

Poltem PV-800 is not compatible with materials have ingredients such as alcohol and water. Because of that, you must sand the product for painting and topcoat application.

You can obtain up to 6 series production with Poltem SW-8 application on the glossy and low risk level moulds.

PACKAGING

The products are packaged in 1 kg tin boxes and 12 tin boxes are packaged in a shrink box.

| Net product weight (g) | 800 |
| --- | --- |
| Gross product weight (g) | 900 |

STORAGE

Keep the product in a dark and dry place at temperatures between 5-20 °C. After using keep it closed. Keep away from flames and electrical sparks. No smoking.